## Slide 1
Isabella Nunes Grieser, T. Gebhard, A. Tundis, J. Kersten, T. Elßner, F. Steinke
Modeling and Monitoring social media dynamics to predict short-term peak electricity demand

## Slide 2: Contents
Motivation
Methodology
  Modeling the Impact of Social Media on Power Demand
  Estimation Algorithm for the Information Spread with Social Media Data
Case Study: Social Media Misinformation Risks in Dynamic Energy Pricing
Conclusion

## Slide 3: Motivation
Bildquelle hier angeben

## Slide 4: Panic Buying and Overconsumption became a prominent topic during the COVID-19 Pandemic
4
Panic Buying: When consumers buy unusually large amounts of a product due to a (perceived) crisis
During the COVID-19 Pandemic: People bought much greater number of disinfectants and soap in fear of the infectious disease.
Panic was amplified due to Information on Social Media
Federal Statistical Office of Germany (Destatis), 2023

## Slide 5: One Example Scenario where Information on Social Media could affect Power Demand
However: other scenarios could be imagined…
Demand Response Scenario:
  Malicious actors compromise the social media channels of an electricity company
  spread the false advertisement of reduced electricity prices for a limited time

## Slide 6: Proposal for a Monitoring Framework
Monitoring Framework:
Predict Model Parameters
Run Simulation with the Proposed Model
Predict Critical Peak Electricity Demand Trend
Collect relevant Social Media Posts
Source: Wikimedia Foundation

## Slide 7: Modeling the Impact of Social Media on Power Consumption
Bildquelle hier angeben

## Slide 8: The Model is divided into three Components
Social Media Graph:
Information Propagation Model:
Power Consumption Rules:

## Slide 9: Graph-Based Social Network Modelling and Information Propagation
Graph model used to model social media networks  Barabási–Albert model
Small world
Scale-free networks
Highly clustered
The SIR model is used to model the information propagation process:
Three states:
  Susceptible (S)
  Infected (I)
  Recovered (R)

## Slide 10: Rule-Based Calculation of the Power Consumption
State Chart:
Recovered
Infected
Susceptible

## Slide 11: The Model is divided into three Components
Assumptions:
Each node in the social media graph represents one (physical) household
Only infected entities change their electricity demand
The effect of the information may have a delayed response on the electrical grid
Simulation Steps:
Start with one source of information
For each iteration step:
  Calculate the power used in the network
  Spread the information in the graph

## Slide 12: Rule-Based Calculation of the Power Consumption
Power Calculation:
Power usage is computed as the normal power consumption + the additional demand:
  Reference power consumption defined with standard load profiles
  Each household may have electrical appliances given their adoption rate
  Households turn on all relevant electrical appliances
  Each appliance consumes a constant amount of energy

## Slide 13: Estimation Algorithm for the Information Spread with Social Media Data
Bildquelle hier angeben

## Slide 14: Social Media Data can be used to estimate Model Parameters
Differential Equations:
 Solve for
Smooth Data Plot
Minimize
Solve Differential Equations
Count Social Media Posts over a Timespan

## Slide 15: CASE STudy
Bildquelle hier angeben

## Slide 16: One Example Scenario where Information on Social Media could affect Power Demand
Demand Response Scenario:
  Malicious actors compromise the social media channels of an electricity company
  spread the false advertisement of reduced electricity prices for a limited time
Assumptions:
Many people believe and will act on the information
Infected entities have a delayed response, acting after the time specified in the social media message
Infected entities will turn on most energy-intensive appliances (dishwasher, washing machine, …) in their households
Number of entities: 1000, time resolution: 30 minutes

## Slide 17: Idea: Use similar, but unrelated information propagation event dataset to estimate realistic model parameters
Social Media Dataset:
  Grunewald fire: Fire caused by an explosion in Grunewald, Berlin on August 4th, 2022
  Posts contained the keywords ” Grunewald”, ”fire”, ”explosion”, or ”bomb”
  Twitter posts and their timestamps gathered between August 4th, 2022, and August 5th, 2022
  In total: 1759 tweets
  Tweets were aggregated to count the number of tweets every 30 minutes
    moving average filter was used to smooth the information propagation plot
Information propagation progress over time for the Grunewald dataset

## Slide 18: Idea: Use similar, but unrelated information propagation event dataset to estimate realistic model parameters
Parameter estimation results with variable data input size

## Slide 19: Simulated Infection Process and Power Consumption
Simulated excess power consumption for different estimated information propagation parameters
Simulated infections process for different estimated information propagation
parameters

## Slide 20: Changes in Power Consumption with a variable adoption rate for EVs
Results of the simulation model with different adoption rates p for EVs

## Slide 21: Conclusion
Bildquelle hier angeben

## Slide 22: Conclusion
Summary:
This paper proposed a framework to monitor the effects of information on the power grid.
  Model to simulate the impact of information on the power grid
  Algorithm to estimate information propagation parameters
Application of our framework on a theoretical scenario
  Usage of similar, but unrelated dataset to analyze our framework
Grid operators and other relevant entities could use our framework to predict critical power consumption peaks caused by information on social media in advance
Results:
Synchronization events caused by information on social media could be critical for the power grid
Increasing adoption of new, highly power-consuming technologies could increase the peak power demand caused by synchronization
Our proposed framework was able to estimate the spread of information successfully, even when the information spread was still ongoing

## Slide 23: Conclusion
Future Works:
Analysis of methods to collect relevant social media posts
  Natural language processing techniques
  Search engine trends
Analysis of countermeasures for changes in power demand based on information on social media
  Currently, only reactive measures, such as load shedding, are considered
  Preemptive countermeasures to prevent removal of consumers from the power grid

## Slide 24: QuestionS?
Bildquelle hier angeben